## Slide 1: Kinematics of Rigid Bodies
Engineering Mechanics

## Slide 2: Introduction to Rigid Body Kinematics
Definition of a Rigid Body:
  A system of particles where distance between any two particles remains constant
Types of Motion:
  • Translation: All points move along parallel paths
  • Rotation: All points move in circular paths around a fixed axis
  • General Plane Motion: Combination of translation and rotation
  • Spatial Motion: Most general 3D motion

## Slide 3: Translation
Key Characteristics:
• All points have identical velocities
• All points have identical accelerations
Key Equations:
Position: ri = ro + rio (constant)
Velocity: vi = vo
Acceleration: ai = ao

## Slide 4: Rotation About a Fixed Axis
Key Parameters:
• Angular position (θ)
• Angular velocity (ω = dθ/dt)
• Angular acceleration (α = dω/dt)
For a point at distance r from axis:
• Linear velocity: v = rω
• Tangential acceleration: at = rα
• Normal acceleration: an = rω²

## Slide 5: General Plane Motion
Combination of translation and rotation
Velocity Analysis:
vB = vA + ω × rBA
Acceleration Analysis:
aB = aA + α × rBA + ω × (ω × rBA)

## Slide 6: Instantaneous Center of Zero Velocity
Definition:
A point in a rigid body (or its extension) that has zero velocity at a given instant
Properties:
• Every point rotates about the IC at that instant
• Velocity vectors are perpendicular to lines drawn from IC
• Velocity magnitude: v = ω × d (distance from IC)

## Slide 7: Relative Motion Analysis
Relative Velocity:
vB/A = vB - vA = ω × rB/A
Relative Acceleration:
aB/A = aB - aA = α × rB/A + ω × (ω × rB/A)
Applications:
• Analysis of connected rigid bodies
• Mechanical linkages
• Slider-crank mechanisms

## Slide 8: Example Problem: Rotating Wheel
Problem:
A wheel rotates according to the relation θ = 2t³ - 3t² + t
(θ in radians, t in seconds)
Find the angular velocity and angular acceleration at t = 2 seconds
Solution:
ω = dθ/dt = 6t² - 6t + 1
α = dω/dt = 12t - 6
At t = 2 seconds:
ω = 6(2)² - 6(2) + 1 = 24 - 12 + 1 = 13 rad/s
α = 12(2) - 6 = 24 - 6 = 18 rad/s²

## Slide 9: Summary
Key Topics Covered:
  • Types of rigid body motion (translation, rotation, general plane motion)
  • Kinematic equations for different motion types
  • Instantaneous center of zero velocity
  • Relative motion analysis
Next Topics:
  • Kinetics of rigid bodies
  • Work-energy principles for rigid bodies
  • Impulse-momentum principles for rigid bodies